Backup and Restore System
# Short Summary
The Backup and Restore system is part of the SBDI deployment platform. It provides the following primary services:
1. Saving a complete and consistent snapshot of all data and configuration of the SBDI system at a given point in time.
2. Restoring any such snapshot of all data and configuration to a running deployment

In other words, if backups are run regularly, in case of for instance a fatal disaster the last, or any valid backup, may be restored and operations may continue from the state that was present at the backup.

Secondary services also provided by the backup system are:
1. Off site backup replication, i.e. all backups are not only stored on the deployment system but synchronized off site.
2. Partial restore of a specific service, like Word Press, email or a specific database.
3. Restore to another deployment which is intended to be used to transfer production data to a test deployment or to another deployment in case SBDI has to be moved.

A key factor important to understanding the Backup and Restore system is that it is designed from the ground up to be a part of the SBDI deployment platform. It is deployed by an Ansible playbook based on the same inventory information that is used to deploy the platform itself. Consequently very little configuration specific to the Backup and Restore system is needed. Also the SBDI deployment platform is designed from the beginning to work optimally with the backup system. This applies to such things as name conventions, where data is placed, network setup, which file systems are used etc.

Also the Backup and Restore system is designed making full use of the fact that SBDI is dockerized. For instance the system uses docker pause and resume in order to ensure the integrity and consistency of backup data. Also the system will manage the docker swarm when backups are restored in order to ensure the integrity and consistency of backup data.

# Intended use of this document
The intended use of this document is that a reasonably experienced Linux systems administrator should be able to fully understand how the Backup and Restore system is designed, installed, maintained and how it may be operated and further developed.
# Status

As of September 2022 primary services are fully implemented and tested (with sample data) and ready for automated use.
Secondary services, except off site replication, are implemented, not fully tested and not automated. In order to use those functions initiated manual operations are required. Off site replication is based on ZFS replication and thus implemented but, as of now, needs to be configured and setup manually.

# Design principles
This section is intended to provide knowledge about how the Backup and Restore system works and why as well as on how to maintain it.
Since the Backup and Restore system has not been fully deployed also possible future problems and how to resolve them are addressed.
## Terms used
A backup or a restore of a backup is initiated and controlled by a Backup Director Node.
Parties involved in the backup holding data are referred to as Backup Source Nodes.
Backup Source Nodes may either hold global data stored on Gluster (explained below) or hold local data stored on LVM (also explained below).
The objective of a backup is to transfer/synchronize and store all data that is to be backed up from the Backup Source Nodes to a Backup Target Node. The data backed up should represent one instance in time, i.e. the data on the Backup Source Nodes should be somehow “frozen” at the same time and then transferred to the Backup Target Node. If the data saved in a backup is a complete representation from one instance in time it may safely and successfully be restored and operations may continue, as if nothing had ever happened, since the point in time when the backup was taken.
The Backup Target Node holds a number of backups, that represent the sate of the system at the time the backups where taken. Backups stored on the Backup Target Node are stored incrementally, i.e. each backup are not stored completely and separately but rather the change from the last backup is stored. This procedure is essential in order to save space. Furthermore data stored on the Backup Target Node is compressed to save space. In practice we can hold dozens of backups on a disk space probably less than what is used by the running system. Backups on the Backup Target Node are also stored in such a way that any one single backup may be accessed and restored to the running system. How this is implemented is covered below.
The final node in a complete Backup and Restore system is the Remote Backup Server. The Remote Backup Server is running at a different geographical location so that its data is kept safe even if the Backup Target Node is totally destroyed. The Remote Backup Server will hold exactly the same data as the Backup Target Node, i.e. data is synchronized/replicated. Since the Remote Backup Server is remote, data replication from the Backup Target Node is not instant but rather synchronized/replicated as an ongoing process.
## The phases of a backup
1. The Backup Director will order Docker to pause all docker containers in the system
2. The Backup Director will order, in parallel, all Backup Source Nodes to create snapshots (frozen images) of data to backup.
3. The Backup Director will order Docker to unpause all docker containers in the system. This stage will be reached in a matter of seconds and from now on systems operations may go on uninterrupted. Users of the system will (hopefully) have experienced only a short delay of a few seconds.
4. The Backup Director will order all Backup Source Nodes in sequence (one at a time) to synchronize there snapshot of data to the Backup Target. This is the time and resource consuming stage of the backup. It may continue for hours but it does not interfere with the normal systems operations.
5. When the synchronization is completed the Backup Director will order the Backup Target Node to save all data (representing the complete backup) as a tagged complete backup, i.e. a ZFS snapshot (as explained below).
6. Finally the Backup Director will order, in parallel, all Backup Source Nodes to remove the snapshots (frozen images) of data.
## The backup restore
Before the restore of a backup all operations in the system must be terminated.
The first step is to stop all Docker services system wide. There is command to do that available on the Backup Director.
The restore operation is conducted by the Backup Director. It will:
1. Order the Backup Target to activate the desired backup, i.e. mount it locally.
2. Order the Backup Target to sequentially restore the data of each Backup Source Node
3. Finally the Backup Director will order the Backup Target to deactivate the desired backup.
When a backup has been restored all Docker services system wide should be restarted. There is command to do that available on the Backup Director. When Docker services have been restarted the system state should then ideally have been restored to that of the backup.
## Gluster and gluster snapshots
The deployment platform uses GlusterFS (https://docs.gluster.org/en/latest/) to store docker swarm images.
There currently exists only one Gluster volume called docker that is provided by the nodes manager-[1..3]. This gluster volume is mounted at /docker on all host nodes of the docker swarm. In the filesystem mounted under /docker all SBDI docker volumes (except Cassandra and Solr) as well as configuration resides in a well defined directory structure.
Thus by taking a snapshot of the docker Gluster volume and rsyncing it to the backup target node we may backup all SBDI containers (except Cassandra and Solr) in one strike.
To snapshot the Gluster volume we rely on Gluster (https://docs.gluster.org/en/main/Administrator-Guide/Managing-Snapshots/) thus fore instance we have to use thinly provisioned LVM on the manager nodes.
During backup a snapshot of the Gluster volume is taken on the manager-1 node and mounted at /gluster_backupsource after rsyncing that filesystem to the backup target the snapshot is removed.
It is worth pointing out that during the time of the rsync the Gluster snapshot will gradually take up more and more space as the SBDI system performs its task (backup does not interrupt operations). It is essential to make sure there is enough space on the thinly provisioned LVM backing device to support that growth. In essence it might not be a good idea to import or process a lot of new data into the system or make big changes during the rsync phase of the backup.
## Logical volume based local storage
The deployment platform uses LVM to store Cassandra and Solr data locally. The backup system makes use of that in order to backup that data.
The local data for Cassandra and Solr is kept on a logical volume called lv_docker_local that is mounted at /docker_local.
During a backup the backup system will, using parallel ssh, take snapshots of the lv_docker_local volumes on all Cassandra and Solr nodes and mount the snapshots at /local_backupsource.
After using rsync to synchronize the data under /local_backupsource to the backup target host the snapshots are unmounted and removed.
Since parallel ssh is only parallel and not transactional all docker containers are paused in the entire SBDI system prior to taking the snapshots to ensure that all snapshots are a consistent representation of the data of the system at that time.
As with the Gluster snapshots also LVM snapshots grow when the data changes on the filesystem they are derived from. Since backup does not interrupt SBDI system operations it is important to ensure that there is enough space on the device backing the LVM. It is therefore suggested that large imports of data sets or indexing operations are not undertaken during backup.
## ZFS Backup Target
It is easy to confuse the term “backup target”. One might think of it as either the data that we intend to backup (probably the most natural association?) or the result of the backup procedure, i.e. the backup itself. We use the second alternative and thus with “backup target” we refer to the the desired result and representation of a backup.
For backup storage ZFS (https://openzfs.org/wiki/System_Administration) and ZFS snapshots and clones (https://ubuntu.com/tutorials/using-zfs-snapshots-clones#1-overview) in combination with high compression (gzip-7) are used.
Piggy backing onto ZFS we will get incremental backups (snapshots), low disk usage (high compression), data synchronization (ZFS off site replication) in combination with proven high grade data safekeeping for free.
ZFS snapshots[1] are used in order to earmark individual backups.
[1] The concept of a snapshots in ZFS and LVM differ slightly. In LVM a snapshot is something that can be accessed and mounted. In ZFS a snapshot may not be accessed. To access it a Clone has to be created from the snapshot. Clones may then be mounted.
### Possible week points
Backup and Restore system has not been tested with full SBDI data volumes. If it happens backups tend to be very it might be worth considering that:
1. High performance ZFS is known to be RAM and CPU hungry, the backup target node may have to be provided with more of those.
2. Tuned ZFS that are performing large amounts of synchronous writes may benefit from a ZIL cache. A backup does most likely involve a large amounts of synchronous writes but a ZIL cache, i.e. a fast SSD may not be added in the intended Open Stack deployment. How to handle this type of performance problem in this case has to be investigated.
3. The writer of this document has previous experience with performance degradation of ZFS in virtual machines when the disk is provided via network such as is the case both at SNIC and NRM. The use of ephemeral disk would probably be much better if performance turns out to be degraded.
The above are examples of possible problems that may or may not occur. It is however a fair assumption that ZFS will be able to deliver good enough performance at lest for normal incremental dayly backups. With a full scale first backup of ~ 5TB+ however things become more uncertain.
An alternative to ZFS might be btrfs (https://btrfs.wiki.kernel.org/index.php/Main_Page) but there is no reason at this point to expect better performance. Btrfs is mentioned here only since it provides a similar functionality as ZFS.
Important: In case of performance issues other possible bottlenecks, other than ZFS, must also be considered like rsync and network performance.
## Rsync
Backups make use of rsync in order to transfer data to the backup target server (https://en.wikipedia.org/wiki/Rsync). On paper rsync is absolutely ideal for the intended use since it only transfers those files that has been changed which in normal SBDI case on a day to day basis is merely a tiny fraction of all files.
SBDI is normally a “read only” system since big changes occurs only when new data sets are imported. This should make incremental daily backups based on rsync very fast.
Important: Since SBDI data consists of a very large quantity of small files it is important to test performance and consider tuning when the SBDI system is fully loaded with data.
### Possible problems with performance
Since we are running rsync over ssh all communication is encrypted. This is a good candidate bottleneck for performance. Following is just a couple of suggestions that may be tried if backups turns out to takes days in stead of hours:
1. Use a lighter encryption algorithm, i.e. like -e "ssh -c arcfour".
2. Do not use any encryption - for instance with HPN-SSH (https://www.psc.edu/hpn-ssh-home/). This should be acceptable, w.r.t. security, since the internal network of the SBDI deployment platform is well protected.
3. Consider removing atime[2] from snapshot file systems mounts. Since atime might impose a lot of network traffic in the underlying OpenStack network file system layers.
  [2] https://www.howtogeek.com/517098/linux-file-timestamps-explained-atime-mtime-and-ctime/
4. Consider using rsync with --whole-file option or possibly with compression -z.
5. Consider using jumbo frames[3], i.e. MTU 9000 networking.
  [3] https://en.wikipedia.org/wiki/Jumbo_frame
It is important to realize that accepting terrible performance should not be necessary. The basic design should be able to perform well. Tuning it to swiftness however might involve a lot of systematic work.
## SSH and parallel ssh
The Backup and Restore system entirely relies on ssh in order to execute its distributed task.
When taking and removing snapshots parallel ssh is used since all snapshots not only can but must be taken at the same instance in time in order to ensure the consistency of the backup. If that is not the case, when backups are restored, internal services in the system might be out of sync.
When syncing backup data from the snapshots to the backup target server these rsync tasks are performed in sequence. This is by design since it is reasonable to assume that running several rsync tasks in parallel against one backup target server will most likely slow down operations.
Furthermore the rsync phase does not have to be performed in a hurry since the data to backup is kept safe on the snapshots.
### Introduce more parallelism to speed up backups
In case backups turn out to be to slow to be practical and tuning, as suggested in other sections of this paper, turns out to not solve the issue there always remains the option of introducing more than one backup target. The general idea here is that the backup system works precisely as now but that the backup is divided up, for instance one backup target node per Solar and Cassandra nod.
Although it is very possible to achieve this parallelism it will complicate the design. It is mentioned here just to indicate a possible solution if the problem with sequential rsync turns out to be a major one.
## The backup structure
The structure of the backup is intentionally kept simple. On the Backup Target the current (last) backup is mounted at /backup/current as illustrated by:
/backup/current# ls -1
cassandra-1@+docker_local
cassandra-2@+docker_local
cassandra-3@+docker_local
cassandra-4@+docker_local
manager-1@+docker
solr-1@+docker_local
solr-2@+docker_local
solr-3@+docker_local
solr-4@+docker_local

Under each of these directories we will find the files and directories as they where, for instance at /docker_local on host cassandra-1, at the time of the last backup.
(Note that ‘/’ may not be used in filenames and has been replaced by ‘+’. Also the ‘@+’ separator are made up of posix filesystem characters that and extremely unlikely to occur in any host name.)
Important: Do not provide virtual machines in an SBDI deployment platform with names including ‘@+’ since it will break the backup functionality.
## Backup portability
Note that in the above section on backup structure host names like cassandra-1 and instead of uat-cassandra-1 or prod-cassandra-1 are used. In the SBDI deployment platform, as specified in the inventory like
# Deployment specific vars
# ========================

[all:vars]
deployment_prefix=uat
...
uat and prod are referred to as a deployment prefix. This concept is made use of in order to be able to deploy SBDI in such a way that there are nothing that is different other than this host name prefix between for instance, test, staging (uat) and production (prod) deployments.
In the Backup and Restore system this design principle is made use of in such a way that it is possible to restore a production backup in staging deployment without transforming any data.
### Procedure to restore production data in staging
In order to restore production data in staging do the following:
1. Shutdown both staging and production backup target nodes. They will be called uat-backup-target and prod-backup-target respectively.
2. Unattach the staging backup data volume from the staging backup target node. It is called uat-backup-target-volume_backup.
3. Unattach the production backup data volume from the production backup target node. It is called prod-backup-target-volume_backup.
4. Attach the production backup data volume to the staging backup target node.
5. Start the staging backup target node
6. Restore the the backup on the staging backup target node
Production data will now be restored in staging.
## Security
The backup operator user has access to almost all machines in the system and must have root access in order to read and restore data and system state. In order for such a powerful system agent not to be able to bad things in case of malfunction, incorrect setup or if it is compromised the following patterns and principles have been followed in the design of the Backup and Restore system:
The backup operator is an unprivileged user without a password, i.e. it can not do general sudo “on its own” and it is not possible to login as backup operator as exemplified by:
$cat /etc/passwd | grep backupoperator
backupoperator:x:1901:1901::/home/backupoperator:/bin/bash

$cat /etc/shadow | grep backupoperator
backupoperator:!:19117:0:99999:7:::

$cat /etc/group | grep backupoperator
backupoperator:x:1901:

1. The privileged operations that the backup operator performs have (with one exception – see below) been capsuled into only a few scripts that needs to be run with sudo, i.e. these capsule scripts include the various low level commands that on their own (not encapsulated) may be used to do many other (potentially harmful) things.
2. These scripts have no arguments or switches of functional character, i.e. if they do not have bugs they are not supposed to be used for performing any other (potentially harmful) task than their intended.
3. Further more these scripts (if there are no bugs in the Ansible installation tasks!) have been given file permissions ensuring that they may not be modified without root access as exemplified by the scripts on the manger-1 node:
/opt/sbdi/backup/bin# ls -lrth
total 48K
-rwxr-xr-x 1 root root 422 May 5 14:51 start_docker
-rwxr-xr-x 1 root root 441 May 5 14:51 stop_docker
-rwxr-xr-x 1 root root 617 May 5 14:51 pause_containers
-rwxr-xr-x 1 root root 634 May 5 14:51 unpause_containers
-rwxr-xr-x 1 root root 3.5K May 5 14:52 prepare_source_snapshot.gluster.sh
-rwxr-xr-x 1 root root 2.1K May 5 14:52 remove_source_snapshot.gluster.sh
-rwxr-xr-x 1 root root 4.1K Jul 14 12:44 prepare_source_snapshot.lvm.sh
-rwxr-xr-x 1 root root 2.5K Jul 14 12:44 remove_source_snapshot.lvm.sh
-rwxr-xr-x 1 root root 341 Sep 2 07:50 prepare_source_snapshot
-rwxr-xr-x 1 root root 2.0K Sep 2 07:50 perform_rsync
-rwxr-xr-x 1 root root 341 Sep 2 07:50 remove_source_snapshot
Also these scripts are generated by the Ansible installation tasks in such a way that all configuration is hardcoded into the scripts, i.e. there are no configuration files (that may be manipulated or include incorrect settings).
Thus the template script file ansible/roles/backup/source/templates/bin/prepare_source_snapshot :
#! /bin/bash
#
# Prepare source snapshot
# =======================

# Note! This script is generated from a template by Ansible
# ---

bin_dir=$(dirname $0)
lib_dir=/opt/sbdi/lib

. $lib_dir/log_utils
[ $EUID -eq 0 ] || log_fatal 88 "Root privileges reqiured"

{% if gluster_backup_source %}

$bin_dir/prepare_source_snapshot.gluster.sh {{ gluster_backup_source_volume }} {{ gluster_backup_source_snapshot_mount_point }}

{% endif %}

{% if lvm_backup_source %}

$bin_dir/prepare_source_snapshot.lvm.sh {{ lvm_backup_source_volume_group }} {{ lvm_backup_source_volume }} {{ lvm_backup_source_snapshot_mount_point }}

{% endif %}

will be expanded by Ansible on the manager-1 node, that holds data to backup on Gluster, to become:
#! /bin/bash
#
# Prepare source snapshot
# =======================

# Note! This script is generated from a template by Ansible
# ---

bin_dir=$(dirname $0)
lib_dir=/opt/sbdi/lib

. $lib_dir/log_utils
[ $EUID -eq 0 ] || log_fatal 88 "Root privileges reqiured"

$bin_dir/prepare_source_snapshot.gluster.sh docker /gluster_backupsource

and on the cassanadra-1 node, that holds local data to backup on LVM, it will be expanded as:

#! /bin/bash
#
# Prepare source snapshot
# =======================

# Note! This script is generated from a template by Ansible
# ---

bin_dir=$(dirname $0)
lib_dir=/opt/sbdi/lib

. $lib_dir/log_utils
[ $EUID -eq 0 ] || log_fatal 88 "Root privileges reqiured"

$bin_dir/prepare_source_snapshot.lvm.sh vg_docker_local lv_docker_local /local_backupsource

Finally these scripts are are “enabled” and made available to the backup operator by means of Linux /etc/sudoers.d (For a general introduction look at for instance https://help.ubuntu.com/community/Sudoers & https://superuser.com/questions/869144/why-does-the-system-have-etc-sudoers-d-how-should-i-edit-it).
To exemplify this, on manager-1, in /etc/sudoers.d , Ansible will install the file 43-backupoperator :
# Ensure backupoperator can transfer ssh agent when sudoing:
Defaults env_keep+=SSH_AUTH_SOCK

# Commands performed with sudo by backupoperator at a backup-source:

Cmnd_Alias BOP_SRC_SNAP = /opt/sbdi/backup/bin/prepare_source_snapshot
Cmnd_Alias BOP_SRC_SYNC = /opt/sbdi/backup/bin/perform_rsync
Cmnd_Alias BOP_SRC_RM_SNAP = /opt/sbdi/backup/bin/remove_source_snapshot
Cmnd_Alias BOP_SRC_ALL = BOP_SRC_SNAP, BOP_SRC_SYNC, BOP_SRC_RM_SNAP, /usr/bin/rsync

backupoperator ALL=(ALL) NOPASSWD: BOP_SRC_ALL

This will enable the backup operator on the backup director node to (parallel) ssh into all backup sources (including manager-1) and do sudo /opt/sbdi/backup/bin/prepare_source_snapshot as indicated by the following extract of the /opt/sbdi/backup/bin/perform_backup script:

...
parallel-ssh -l backupoperator -i -H "${BACKUP_SOURCE_HOSTS}" 'sudo /opt/sbdi/backup/bin/prepare_source_snapshot'
...
1. There is only one RSA ssh private key, stored on the, backup director node that is used by the backup and restore functions. As explained above this key and the ssh agent is transferred by ssh during Backup and Restore operations. This design has been implemented in order to make it impossible for any other node than the backup director to initiate and run backup or restore operations.
2. The RSA key and all scripts with hard coded configuration may always be regenerated by Ansible. The ansible playbook may be run as may times as desired it will (if correct) generate and distribute a new RSA key and make sure that the Backup and Restore system is attuned to the current Inventory. This is to ensure that no manual (possibly error prone) installation and configuration is needed.
### Remaining security issues to consider

As explained above all Backup and Restore operations are supposed to be based on “capsuled” scripts. Currently this is not 100% since the restore_backup_snapshot script that resides on the backup target node includes the following invokation of rsync over ssh in order to restore backup data:
…
/usr/bin/rsync -a -e /usr/bin/ssh --rsync-path="/usr/bin/sudo /usr/bin/rsync" \
        $dry_run $verbose $rsync_flags \
        /backup/snapshot/${backup_name}/ --delete-after backupoperator@${remote_dest}:${backup_source_dir}
...

This is the reason that on all backup source nodes we need to have an entry in sudoers that allows backup operator to do sudo rsync, like in:
Cmnd_Alias BOP_SRC_ALL = BOP_SRC_SNAP, BOP_SRC_SYNC, BOP_SRC_RM_SNAP, /usr/bin/rsync

This is clearly an exception to the rule since rsync is a very powerful tool. It remains to encapsulate rsync. This can most likely be done (and it is probably a good idea to do so) but this is a notably tricky task possibly best explained by the use of --rsync-path="/usr/bin/sudo /usr/bin/rsync".All in all this solution enable us to do ssh (part of rsync) not as root but as backup operator while still allowing rsync to have needed (root) power in order to restore data. Doing ssh as root, which is the other alternative, is a much bigger vulnerability than having rsync in /etc/sudoers.
There is also a corresponding entry in /etc/sudoers.d/42-backupoperator that allows sudo rsync that is needed for the taking of backup:
Cmnd_Alias BOP_TRG_ALL = BOP_TRG_SNAP, BOP_TRG_ACT_L_SNAP, BOP_TRG_ACT_SNAP, BOP_TRG_DEACT_SNAP, BOP_TRG_REST_SNAP, /usr/bin/rsync

Since this privilege to do sudo rsync is limited to only the backup target it is deemed less risky than enabling sudo rsync on all backup source nodes.
## Docker Swarm integration
To implement a pause or unpause of all docker containers the Backup Director will use parallel ssh to execute the following commands on each host running docker (either in swarm or standalone mode):
CONTAINERS="$(docker container ls --format '{{ .ID }}')"
docker container pause $CONTAINERS
or
CONTAINERS="$(docker container ls --format '{{ .ID }}')"
docker container unpause $CONTAINERS

In order to start or stop docker services Backup Director will use parallel ssh to execute the following command on each host running docker (either in swarm or standalone mode):
systemctl start docker
or
systemctl stop docker.socket

The latter command is necessary since just stop docker leaves docker services running.
## Dependencies
The Backup and Restore system is installed as an integral part of the SBDI deployment platform.
It is assumed that all the parts of the SBDI deployment platform is installed. That is Ansible playbooks corresponding to step 1 through 10 (refer to automation/ansible/README.md) must have been run.
### Logging and supervision
All Backup and Restore operations uses the /opt/sbdi/lib/log_utils package to log progress and errors. /opt/sbdi/lib/log_utils uses a uniform log format that will (although backup operations are distributed onto many different hosts) make it possible to collect syslog streams form all SBDI nodes and filter them in a central logging server. Thus it will be possible to monitor and analyze logging operations as integrated operations. Also in this way it will, for instance by means of a Nagios “probe” script, be possible to issue alerts in case backups are not working or taking to long etc.

Note: Although SBDI deployment platform is designed for centralized logging this is not implemented yet.
## Ansible playbook integration
The backup system is installed and managed by Ansible (https://docs.ansible.com/ansible/latest/).
Important: The playbook is idempotent so the following command will install and, in case the deployment is changed it will reconfigure backup accordingly:
ansible-playbook backup.yml

The playbook runs basically five steps:
1. sets up backup functionality and backup operator user on the backup director virtual machine
2. sets up a backup operator user on all other hosts involved in the backup, i.e. the backup target node and the various backup source nodes.
3. sets up backup functionality on backup target(s) virtual machines
4. enables the backup operator user to control docker swarm when needed
5. sets up backup functionality on all backup source nodes
Important: Do not reconfigure or change the Backup and Restore system directly on the deployed hosts – use the Playbook. Files managed by Ansible might otherwise for example get out of sync.
### 1. The backup director virtual machine
In the Ansible inventory (https://docs.ansible.com/ansible/latest/user_guide/intro_inventory.html#intro-inventory) we must define which virtual machine/node that is designated as backup director:
[backup_director]
backup-director
Any virtual machine in the deployment should be able to serve as backup director but it is recommended (and only tested) with a designated machine with very little CPU and RAM, like in:
[servers]
...
backup-director nbr=91 flavor=ssc.tiny

The tasks involved in setting up the backup director is found in role:
ansible/roles/backup/director

The task of this rule will ensure a backup operator user with an always new ssh key
and .ssh/known_hosts file to ensure scripted ssh operation.
The task also installs parallel SSH (pssh), sets up environment variables and installs the following primary operations scripts:

   perform_backup
    restore_latest_backup
    restore_backup
    stop_docker
    start_docker
    pause_containers
    unpause_containers
    list_backups

The scripts are all well documented code and their operation is as inferred by their names.
One thing worth pointing out however is that the scripts are Ansible templates. When installed by the playbook the various hosts, backup target, backup sources etc are hard coded into the scripts. This is intentional. The scripts may not be altered, due to access rights and they may not be run with arguments. If the setup of the deployment platform changes the backup playbook needs to be run in order to update these scripts.
Please also note the file ansible/roles/backup/director/vars/main.yml defines all hosts involved in the backup based on the inventory.
### 2. Backup operator user
The task ansible/roles/backup/directed sets up a backup operator, with the same gid and uid as on the backup director node, on all the hosts involved in the backup, i.e. the backup target node and the various backup source nodes.
The task also ensures that the backup operator on backup target may use passwordless ssh to access the directed nodes by means of adding the backup operator public key to authorized_key.
The backup operator as such is entirely unprivileged. The ssh key of the backup operator resides only in one copy on the backup director node. If the key is compromised it may be regenerated by running the backup.yml playbook.
The operations that may be run by the backup operator, with root privileges, is defined by sudoers configuration files also generated by the backup.yml playbook.
In order to run backup operations one must log into the backup director node an su to the backup operator user. However since the backup operator does not have a password one must have root access to the system in order to perform backup operations.
### 3. The backup target node
The task ansible/roles/backup/target is well annotaded. Most importantly it installs ZFS and sets up a ZFS pool (if needed) and makes sure there is a /backup mount point with a ZFS file system mounted.
OIn order for that to work there must be a backup_data_device present.
The backup_data_device is currently configured in the file ansible/groups_vars/backup_targets
Its current default value, i.e.
backup_data_device: /dev/vdb
works when using network provided data volumes (as we currently do) but may have to be adjusted in other setups.
Also note the following setting in the inventory file:
[servers]
...
backup-target nbr=92 flavor=ssc.medium.highmem volume_backup=1500

The volume_backup variable is used in the playbook
automation/ansible/deploy.yml

and its subordinate role
automation/ansible/roles/deploy/storage_volumes/tasks/main.yml

where it will be used to attach an OpenStack disk volume, with correct size, to the Backup Target Node.
Pleas note that due to limitations in OpenStack it is not possible to resize a mounted volume. This makes it complicated to write an idempotent Anisble Playbook to automatically adjust the size of data volumes to specified values. In short the Backup Target Node data volume is setup once by Ansibel but must be manually resized if needed occurs.
In order to resize the backup disk space on Backup Target Node the Backup Target Node first have to be shut down and the volume resized in OpenStack GUI or by OpenStack commands:
After restarting the Backup Target Node the device /dev/vdb will have increased:
# parted -l
Model: Virtio Block Device (virtblk)
Disk /dev/vdb: <larger value than 1611GB here>
Sector size (logical/physical): 512B/512B
Partition Table: gpt
Disk Flags:
Number Start End Size File system Name Flags
 1 1049kB 1611GB 1611GB zfs zfs-f29da1940c667ec6
 9 1611GB 1611GB 8389kB

The problem here is that partion 9 created by ZFS is blocking a
parted /dev/sdb resizepart 1 100%

that we would like to issue in order to make it possible for ZFS to take advantage of the extra space now available on /dev/vdb.
This is a consequence of not providing ZFS with disks to manage as it is designed to have. We may not do that, since we are running on OpenStack, and thus we have to work around this problem.
In order to avoid this problem it is by far easiest to allocate enough disk space from the beginning when the Backup Target is deployed[4].
If expanding space is necessary this is possible. There mater is discussed in for instance https://serverfault.com/questions/946055/increase-the-zfs-partition-to-use-the-entire-disk.
It might work just to remove the 9’th partion and let parted resize the disk. In case production data backups are stored on the disk it might be vise to try this out and develop a resizing a procedure in a test deployment first. Also with off site replication in place the risks associated with destroying data is lower.
[4] Unfortunately we have a shortage of disk space on the current uat installation and only 1.5 TB have been allocated.
### 4. Docker swarm control
The task ansible/roles/backup/docker_control is simple and well annotated. It installs the scripts involved for docker daemon control (start_docker, stop_docker, paus_containers, unpause_containers) and configures sudoers rights on all nodes running docker.
Please note that there are scripts with the same name on the Backup Director Node[5]. These “director scripts” that coordinate starting, stopping etc in the system must not be confused with the once installed on the nodes running docker.
[5] In case the Backup Director is merged with a Backup Source node this will become a problem that has to be solved.
### 5. The backup source nodes
The task ansible/roles/backup/directed basically sets up a backup operator user on all nodes that are controlled by the Backup Director.
The task ansible/roles/backup/source does:
Ensures mount points for snapshots (either LVM or Gluster)
Installs scripts for creating and removing snapshots (either LVM or Gluster)
Enables suoders rights in order to allow the backup operator sudo rights to these scripts
Ensures root ssh access to backup target, i.e. updates /root/.ssh/known_hosts. This might seem tricky but is necessary because rsync does the reading of backup data as root but it will ssh as backup operator user.
After some refactoring it was decided to make backup sources explicit in the inventory. Of course it is possible to deduce this information but explicit clarity was decided a better option. Consequently now the backup sources must have a section of their own:

[backup_sources]
manager-1 gluster_backup_source=True lvm_backup_source=False backup_snapshot_storage=0
cassandra-1 gluster_backup_source=False lvm_backup_source=True backup_snapshot_storage=20
cassandra-2 gluster_backup_source=False lvm_backup_source=True backup_snapshot_storage=20
cassandra-3 gluster_backup_source=False lvm_backup_source=True backup_snapshot_storage=20
cassandra-4 gluster_backup_source=False lvm_backup_source=True backup_snapshot_storage=20
solr-1 gluster_backup_source=False lvm_backup_source=True backup_snapshot_storage=20
solr-2 gluster_backup_source=False lvm_backup_source=True backup_snapshot_storage=20
solr-3 gluster_backup_source=False lvm_backup_source=True backup_snapshot_storage=20
solr-4 gluster_backup_source=False lvm_backup_source=True backup_snapshot_storage=20

As noted this is very explicit and there is room for improvement but as for now the variables gluster_backup_source, lvm_backup_source and backup_snapshot_storage needs to be explicitly specified.
gluster_backup_source and lvm_backup_source may currently not be both true.
backup_snapshot_storage is irrelevant for gluster volumes and should be set to 0
backup_snapshot_storage for LVM local storage nodes is used by the playbook
automation/ansible/deploy.yml

in order to ensure there is enough space for the snapshots on the volumes attached to the nodes.
Please note that at present how big the snapshots will be during normal operation is unknown and dependent on usage of the system currently not possible to measure. Therefor it is strongly reccomended that during a stress test of the system a backup is also run and the LVM snapshot sizes are closely monitored. Alternatively assign a very large upper limit, i.e. not 20GB but rather 100GB.
# Operations reference
In order to take a backup the administrator first needs to log into the backup director node and become backup operator. On the uat system this translates to:
### To access backup operations

$ ssh -J uat-access-1 uat-backup-director
$ sudo su – backupoperator

Backup operation commands are found in the /opt/sbdi/backup/bin/ directory
Important: Backup operations may take a long time and if interrupted complicated manual “cleaning up” might be necessary. In order to minimize the risk of that happening it is recommended to run the following operations in a GNU Screen shell, or similar, (https://www.gnu.org/software/screen/) in order to be able to detach the shell without interrupting unfinished work.
### To list existing backup operations
$ cd /opt/sbdi/backup/bin/
/opt/sbdi/backup/bin$ ls -1
list_backups
pause_containers
perform_backup
restore_backup
restore_latest_backup
start_docker
stop_docker
unpause_containers
### To run a backup

/opt/sbdi/backup/bin$ ./perform_backup
…
### To list existing backups
/opt/sbdi/backup/bin$ ./list_backups
20220906_082043
20220903_003826
...

Backups are listed by a date and time string. Such a string is also the backup identifier .
### To restore backups
In order to restore a backup the docker services on all nodes must be shut down
/opt/sbdi/backup/bin$ ./stop_docker

When all docker services have been shutdown we may restore a specific backup by identifier like:
/opt/sbdi/backup/bin$ ./restore_backup 20220903_003826

We may also restore the last backup and then no backup identifier is needed:
/opt/sbdi/backup/bin$ ./restore_latest_backup

Finally when the backup has been successfully restored all docker services in the platform must be restarted:
/opt/sbdi/backup/bin$ ./start_docker
### Pausing and unpausing docker containers
During a backup operation just before file system snapshots are taken the backup system pauses all containers. That is to ensure that local data on the various docker swarm nodes are in sync. After the snapshot has been taken all containers are unpaused. This is a safety precaution and will stop all operations for a few seconds.
Pausing and unpausing is handled by the perform backup command automatically and there is no need for the backup operator to use them explicitly.
The pause and unpaus commands are however also made available to the backup operator explicitly since they might be handy operations for various reasons. Remember to use them with caution since they will freeze all SBDI operations and may thus have any number of spin off effects.
## Automating backup
It is possible to automate the backup procedure with, for instance, crontab (https://www.adminschoice.com/crontab-quick-reference).
Keep in mind if crontab is used to make sure that:
1. The perform backup command is run by cron as a backup operator user
2. The backup operator environment variable DOCKER_HOSTS is set. This environment variable is set by Ansible in the /home/backupoperator/.bashrc file.
Note of caution: Currently the backup system has not been “battle tested”. It is suggested that automated backups are introduced when there are supervision implemented, i.e. Nagios, that monitors success. Also it is suggested that manual backups are performed for a suitable time in order to ensure that it works without “hiccups”.
# Way forward – remaining issues
The SBDI deployment platform is currently not fully tested and operational. Some features of the backup systems are (because of lack of time) not yet in place.
In the above sections many remaining issues, possible problems and some hints on how to solve them have been included. In this section we will shortly address off site backup replication and performance.
## Off site backup replication
ZFS has built in functionality for off site replication. With ZFS snapshots (like current) backups may either be sent or pulled from the Remote Backup Server.
In the SBDI case all that is needed is to make sure the Remote Backup Server is accessible from the Backup Target Server via ssh. This can be done in many ways. One way is by making use off the existing IP Sec server, i.e. connect-1, to setup a tunnel (initiated by the Remote Backup Server).
Then after a backup has been saved on the Backup Target all that needs doing is spawning a job that does the equivalent of:
# zfs send backup/current@snap_20220906_082043 | ssh <remote_backup_server> zfs recv backup/current
The following article elaborates this better: https://www.howtoforge.com/tutorial/how-to-use-snapshots-clones-and-replication-in-zfs-on-linux.
Things to consider here is root access. It is suggested that the unprivileged bakupoperator user is given sudo rights (by means of /etc/sudoers) in order to run the ZFS commands send and receive as needed.
Since fully implementing off site backup replication includes a lot of implementation work like Anisble scripts, setting up users, ssh access, handling errors, spawning jobs, logging etc it is suggested that making use of an existing application like TrueNAS (https://www.truenas.com/) is considered. TrueNAS has easy to access graphical configuration capabilities built in to setup ZFS replication. In this case if the Remote Backup Server was a TrueNAS installation it would be easier to simply grant TrueNAS ssh access to the Backup Target Server and configure a “pull” synchronization.

## Performance
Transferring 5TB (like a full backup) on a 5Gbit network will not take less than 1000 * 8 seconds ~ 2 hours and 15 minutes.
Writing or reading 5TB of data to fast industry standard SSD disks with 500MB/s bandwidth takes no less than 10 * 1000 seconds ~ 2 hours and 46 minutes.
No matter how optimized the Backup and Restore system is we will have to expect not to be able to perform a full backup in shorter times than that.
In the last tests performed we measure times close to 25 hours for backing up 0.5 TB. Incremental backups are significantly faster but we have not been able to test how fast in practice. Thus we have an indication of performance 100+ times slower than best possible.
Is this cause for worry?
Unfortunately that is not possible to say. Early indications however are that using network provided disk as in our case might make the backup system very slow and possibly even too slow.
What to do?
1. Increase CPU and RAM
2. Use faster MTU 9000 networking
3. Try performance optimizations as suggested above, noatime, faster or no encryption, etc
4. Use ephemeral disk, i.e. local disk
5. Do not backup Cassandra and Solar data
6. Use another backup strategy/system
Experiences this far suggests that OpenStack network provided volumes might not make SBDI perform fast enough even with all possible tweaks. Even though this remains to be tested with lots of data during imports and indexing we have strong indications that Ephemeral disk is a better option[6].
[6] During development of the first SBDI installation ephemeral disk had to be used in order to make some functions like Cassandra usable.
The strategy not to backup Cassandra and Solr may actually be the most obvious way to go. Cassandra has in itself support for replication and all data in Solr may be recreated by SBDI itself. In additon to this when pipelines are introduced in SBDI Cassandra will no longer be used for records storage.
The option to use another backup strategy or system altogether should be give careful consideration. In general terms the Backup and Restore system described in this document provides a solution that makes integrated use of probably the fastest and most proven open source technologies available, i.e. LVM snapshots, Rsync, SSH and ZFS. Designing a faster solution with a similar or comparable mode of operation but maybe with other components will be difficult. What may make the current solution impractical or not usable most likely relates to the fact that it is run within a highly complex complex, i.e. Open Stack, where issues with virtual network provided storage, virtual networking etc might interfere destructively with its intended operation.
What might be worth considering if OpenStack with virtual network provided storage is unavoidable and no performance tweaks as suggested does suffice is to use disruptive technology altogether. Such disruptive technology in this case would indicate that the backup solution should be an integral part of Open Stack. And there are solutions in OpenStack that may be used. In Open Stack it is possible to take snapshots of Virtual Machines as well as data volumes. This will be magnitudes faster but how are these functions to be orchestrated and provide a similar operation as this Backup and Restore system? How do we use these functions to take a backup of data and load it into a staging environment? How do we ensure that all the virtual machines and data on the data volumes are backed up at the same instance? The very idea with Using Open Stack for instance is not to have to worry about the internals of Open Stack.
In order to develop an alternative solution, with better performance, lateral thinking in combination with another innovative approach altogether is probably needed.
# Overview reference
Following is an overview diagram of the Backup and Restore system:

BackupSourceServer
Plain LVM
BackupSourceServer
Plain LVM
BackupTargetServer
ZFS
BackupDirector
BackupSourceServer
Gluster
”Y”
Gluster

BackupSourceServer
”Plain” LVM
X1
LVM

> pssh perform_backup (1)
prepare_sourece_snapshot (2y)
Gluster
snapshot

remove_source_snapshot (4y)
LVM
snapshot

remove_source_snapshot (4x1)
prepare_source_snapshot (2x1)
performe_rsync (3y)

snapshot_backup(5)
RemoteBackupServer
ZFS

zfs replication

y
x1

performe_rsync (3x1)
# Acknowledgment
The Backup and Restore system described in this document was originally developed by Hans Höök at Altrusoft AB as part of the open source AltruSOMO project. It has been tested and used in production for over 10 years. Since the AltruSOMO code was taken off line, when Altrusoft ended operations, the code developed for SBDI have been retrieved from private copies and revised and refactored to fit SBDI. The biggest improvements from the original code is the integration with Ansible and Docker Swarm.
The parts used from the AltruSOMO project is made available as Open Source Software published under the GNU Lesser General Public License version 2. Copyright (c) 2009, Altrusoft AB.